## Slide 1
Smart Motion Detection
IoT Security Infrastructure Powered by ESP32 & Cloud Analytics
ESP32 Microcontroller
HC-SR501 PIR Sensor
Blynk + ThingSpeak Cloud
github.com/ThanhTu-Micop/PIR-motion-detection
Notes: Welcome. This is the Smart Motion Detection System — an IoT security device built on the ESP32 microcontroller, using a HC-SR501 PIR sensor and dual cloud backends (Blynk + ThingSpeak).

## Slide 2
THE PROBLEM
Why Smart Motion Detection?
Passive Systems
Traditional alarms require manual activation and can't adapt to environment or report events remotely.
Delayed Response
Without real-time cloud connectivity, intrusion alerts are delayed, reducing effectiveness and auditability.
No Analytics
Conventional sensors provide no historical data for pattern recognition, audit trails, or security analysis.
✓ Our Solution: An ESP32-based smart alarm system with cloud telemetry, mobile control & analytics

## Slide 3
PART 01
Hardware Engineering
Designing for Physical Stability and High-Fidelity Signal Processing

## Slide 4
PERIPHERAL MAP & PINOUT
HARDWARE UNIT
GPIO
SIGNAL PROTOCOL
SYSTEM LOGIC ROLE
PIR Motion Sensor
27
Digital Input
Captures infrared heat signatures via Fresnel lens. Triggers interrupt on movement.
Active Buzzer
26
Digital Output
Localized acoustic deterrent — Active High (85dB+) on intrusion detection.
System Status LED
25
Digital Output
Visual strobe synchronized with alarm state for instant local indication.
Notes: 3 components are wired to the ESP32: PIR sensor on GPIO27, buzzer on GPIO26, LED on GPIO25.

## Slide 5
PHYSICAL STABILITY
Industrial Interconnects
To eliminate the 'messy wire' syndrome and ensure system longevity, the prototype was upgraded with permanent hardware fixes for production-grade reliability:
Female Header Sockets
The ESP32 is mounted on soldered header blocks to prevent vibration-based signal dropouts and enable easy module swaps.
Housing Connectors
All sensor and actuator cables are grouped into polarized black housing plugs, preventing miswiring and simplifying maintenance.
Ruggedized Wiring
Twisted cable pairs reduce electromagnetic interference on sensor lines, ensuring clean digital signal transmission.
ESP32
Microcontroller
GPIO 27
PIR Sensor
GPIO 26
Buzzer
GPIO 25
LED Strobe
3V3/GND
Power Rail
Wi-Fi
Cloud Link

## Slide 6
LOCAL RESPONSE MATRIX
Immediate on-device alarm responses — no internet connection required
Pin 26
Audio Deterrent
Active piezo buzzer generates 85dB+ alerts upon intrusion detection. Frequency modulated for maximum audibility.
85dB+
Sound Pressure
Pin 25
Visual Strobe
High-visibility LED strobe triggers instantly upon alarm state, providing clear visual warning to occupants.
<10ms
Response Time

## Slide 7
PART 02
IoT & Cloud Ecosystem
Merging Edge Computing with Cloud-Based Telemetry

## Slide 8
DUAL-CLOUD INTEGRATION
ThingSpeak Channel ID: 3402569 · 3 Data Fields: Detection Count, Hour, Minute
Blynk IoT
Interaction Layer
Real-time remote arm/disarm via Virtual Pin V0. Live gauge monitoring and push notifications to mobile.
App Control
ThingSpeak
Database Layer
Time-series logging of all detection events. 3 fields: Detection Count, Hour, Minute for full audit trails.
Analytics
NTP Sync
Timing Layer
Real-time clock synchronization via Network Time Protocol for precision event timestamping across platforms.
Precision Time

## Slide 9
SYSTEM WORKFLOW
End-to-end event lifecycle from detection to cloud logging
01
Sensing
PIR Detection
HC-SR501 identifies IR shift. GPIO 27 pulled HIGH, triggering ESP32 hardware interrupt routine.
Sensing
02
Reaction
Local Alarm
Buzzer (Pin 26) activates at 85dB+. LED strobe (Pin 25) synchronizes with alarm state instantly.
Reaction
03
Reporting
Cloud Notify
Blynk Virtual Pins updated. Push notification dispatched to mobile. Event logged with NTP timestamp.
Reporting
04
Logging
Audit Trail
Detection count, hour, and minute written to ThingSpeak channel 3402569 for long-term analytics.
Logging
GitHub: github.com/ThanhTu-Micop/PIR-motion-detection

## Slide 10
KEY ACHIEVEMENTS
What We Built & Learned
4
GPIO Peripherals
Sensor · Buzzer · LED · Button
2
Cloud Platforms
Blynk IoT + ThingSpeak
3
ThingSpeak Fields
Count · Hour · Minute
<1s
Detection-to-Alert
Full event cycle time
100%
Offline Capable
Local alarm without cloud
Notes: Summarize the key deliverables. Mention the GitHub repo and ThingSpeak channel as live proof. Thank the audience.